## Slide 1: Southern Rocky Mountain TCN
Georeferencing
Workshop Day 2
September 19th 2019
Ryan Allen
Dina Clark
Tim Hogan
Erin Tripp
University of Colorado Herbarium

## Slide 2: Goals for Today
Southern Rocky Mountain TCN
Tips for collecting data in the field
Georeference Examples from SoRo collections
Create a participant list (add yourself please) https://docs.google.com/document/d/11DrdaI0HvAlcXPsQQL1GNdXKCm8USU8DQ17iaYSam4I/edit

## Slide 3: Collecting Better Field Data
Southern Rocky Mountain TCN
Record the datum from the GPS (better yet set it to WGS84)
Record the Coordinates (use decimal degrees so you do not need to convert it later)
Record the uncertainty (typically under 10 meters if you are getting a good signal)

## Slide 4: Collecting Better Field Data
Southern Rocky Mountain TCN
Do not reference things that change over time.
  In front of the Blockbuster Video
  Yard of the Smith’s House
  Vacant lot on Arapahoe Road.
  Are unstable locations.

## Slide 5: Collecting Better Field Data
Southern Rocky Mountain TCN
Coordinates and TRS are not a substitute for locality data!
If you are taking one point and collecting in an area report that area as the uncertainty (add it to the GPS uncertainty for best results)
MVZ Guide for Recording Localities in Field Notes
  https://www.idigbio.org/sites/default/files/workshop-presentations/ttt2/GoodBadLocalities.doc

## Slide 6
From train the Trainers 2013 workshop Good and Bad Localities https://www.idigbio.org/sites/default/files/workshop-presentations/ttt2/2013_GoodAndBadLocalities.ppt
Vague
Requires specific knowledge
Non-sensical
Biologically unlikely
REAL LOCALITIES FROM MaNIS

## Slide 7: Darwin Core Georeferencing
Southern Rocky Mountain TCN
Term | Definition
decimalLatitude | Latitude
decimalLongitude | Longitude
geodeticDatum | Datum WGS84, NAD 27, NAD83 etc
coordinateUncertaintyInMeters | Uncertainty
footprintWKT | Shape File for polygon based error
verbatimCoordinates | TRS, UTM, Latitude, Longitude
georeferencedBy | Person Who Georeferenced
georeferenceProtocol | Protocol i.e. Georeferencing Best Practices
georeferenceVerificationStatus | Has the record been proofed or reviewed
georeferenceRemarks | Narrative on how the point was determined
verbatimElevation | Elevation (feet), Elevation (meters)
Notes: Additionally georeferenceDate is an accepted term for Darwin Core, but is not part of the Symbiota standards.

## Slide 8: Data Standards for SoRo
Southern Rocky Mountain TCN
Minimum Fields for a Quality Georeference
decimalLatitude/ decimalLongitude
geodeticDatum
coordinateUncertaintyInMeters
georeferencedBy
georeferenceRemarks
georeferenceProtocol
Notes: I would suggest adding georeferenceDate which is not currently part of Symbiota infrastructure. We do this in the georeferenceRemarks field separated with a semi-colon.

## Slide 9: Open the spreadsheet
Southern Rocky Mountain TCN
Enter the link and select the spreadsheet doc at the bottom:
https://www.idigbio.org/wiki/index.php/SoRo_TCN_Georeferencing_Workshop
Direct link:
https://docs.google.com/spreadsheets/d/1Yt_tA-GxWS8tMolgyQkGfBTrr2zJSS-dBPqk2K54tXU/edit#gid=0
Notes: I would suggest adding georeferenceDate which is not currently part of Symbiota infrastructure. We do this in the georeferenceRemarks field separated with a semi-colon.

## Slide 10: Unknown Datum
Error assuming NAD27 vs. NAD83 or WGS84
Notes: Unknown datum will result in an additional uncertainty of between 50 and 100 meters across the SoRo region.

## Slide 11: Locality 1
Southern Rocky Mountain TCN
Location: Farmington, San Juan County, New Mexico
Habitat: none
Elevation: none
Georeference Type: Named Place

## Slide 12: Locality 2
Southern Rocky Mountain TCN
Location: Laramie, Albany County, Wyoming
Habitat: none
Elevation: none
Georeference Type: Named Place

## Slide 13: Locality 3
Southern Rocky Mountain TCN
Location: Spearfish, Lawrence County, South Dakota
Habitat: none
Elevation: none
Georeference Type: Named Place

## Slide 14: Locality 4
Southern Rocky Mountain TCN
Location: Chadron Airport, Dawes County, Nebraska
Habitat: none
Elevation: none
Georeference Type: Named Place, Undefined Area

## Slide 15: Locality 5
Southern Rocky Mountain TCN
Location: Boulder Creek, Boulder County, Colorado.
Habitat: Riparian corridor.
Elevation: 6,000 ft.
Georeference Type: Named Place River, Stream, Road (with elevation)

## Slide 16: Locality 6
Southern Rocky Mountain TCN
Location: Middle Park, Grand County, Colorado.
Habitat: None
Elevation: None
Georeference Type: Named Place, Undefined Area

## Slide 17: Locality 7
Southern Rocky Mountain TCN
Location: Between Farmington and Shiprock, New Mexico
Habitat: none
Elevation: none
Georeference Type: Named Place, Between two areas.

## Slide 18: Locality 8
Southern Rocky Mountain TCN
Location: Rio Grande River HWY 423 Bridge Albuquerque, New Mexico
Habitat: floodplain
Elevation: none
Georeference Type: Named Place, Junction, Intersection, Crossing

## Slide 19: Locality 9
Southern Rocky Mountain TCN
Location: Slopes above Grand Lake, Grand County, Colorado
Habitat: Northeast slope.
Verbatim Coordinates: T2N, R76W, SW ¼ sec 3
Elevation: 8400 ft.
Georeference Type: Coordinates Grid System

## Slide 20: Locality 10
Southern Rocky Mountain TCN
Location: Roadside ditch 1.5 miles north of Lyons, Boulder County, Colorado
Habitat: Roadside ditch.
Elevation: 5480 ft.
Georeference Type: Offset at a heading/ Offset along a path

## Slide 21: Locality 11
Southern Rocky Mountain TCN
Location: Lafayette, Waneka Reservoir, Colorado.
Habitat: none
Verbatim Coordinates: 40°N, 105°W
Elevation: none
Georeference Type: Named Place, Coordinates*

## Slide 22: Locality 12
Southern Rocky Mountain TCN
Location: Valmont Reservoir, Boulder, Boulder County, Colorado
Habitat: none
Elevation: none
Georeference Type: Named Place, Undefined Area

## Slide 23: Locality 13
Southern Rocky Mountain TCN
Location: Road Between Laramie and Cheyenne, Laramie County, Wyoming
Habitat: none
Elevation: none
Georeference Type: Named Place, Between two areas*.

## Slide 24: Locality 14
Southern Rocky Mountain TCN
Location: No location data on the label.
Habitat: none
Verbatim Coordinates: T7N , R69W, NW1/4 Sec 19
Elevation: 5705 ft.
Georeference Type: Coordinates Grid System

## Slide 25: Locality 15
Southern Rocky Mountain TCN
Location: Along Cog Railway, Pikes Peak, El Paso County, Colorado.
Habitat: East slope
Elevation: 8,000 ft.

## Slide 26: Locality 16
Southern Rocky Mountain TCN
Location: Colorado River, Colorado.
Habitat: none
Elevation: none

## Slide 27: Locality 17
Southern Rocky Mountain TCN
Location: Rocky Mountain Biological Laboratory, Colorado
Habitat: none
Elevation: none
Georeference Type: Named Place, Undefined Area

## Slide 28: Homework
Southern Rocky Mountain TCN
Georeference a record out of your collection and come prepared to talk us through how you georeferenced it.
I will also pull a selection of actual specimens that have not been databased out of the SoRo portal and we will georeference them on Tuesday.

## Slide 29: Thanks!
Students and staff that perform the digitization and georeferencing work
Dave Bloom, Nelson Rios, Jessica Utrup, Una Farrell and Deb Paul for their slides from the 2013 Train the Trainers Workshop (https://www.idigbio.org/wiki/index.php/GWG_Second_Train_the_Trainers_Workshop)
J Ryan Allen
Biodiversity Informatics Manager University of Colorado Herbarium
Project Coordinator Southern Rocky Mountain TCN project
James.r.allen@Colorado.edu
Southern Rocky Mountain TCN